Stuart Golodetz														FAO: Dr. G. Jones

Digital Hardware

Problems 3

1.

Commented MIPS version:

begin:

addi $4, $0, 0			# $4 = $0 + 0

addi $5, $0, 1			# $5 = $0 + 1

loop:

slt $6, $2, $5			# $6 = if $2 < $5 then 1 else 0

bne $6, $0, finish		# goto finish if $6 != $0

add $4, $4, $5			# $4 = $4 + $5

addi $5, $5, 2			# $5 = $5 + 2

br loop				# goto loop

finish:

add $3, $4, 0			# $3 = $4 + 0 -> assuming this is

# either (a) an exception to the

# "parameter must be a register"

# thing (b) meant to be addi (c)

# meant to be $0

We translate this to a C++ program to see what’s going on more easily:

Pseudo-C++:

$4 = 0

$5 = 1

while(1)

{

if($2 < $5) $6 = 1;

else $6 = 0;

if($6 != $0) break;

$4 += $5;

$5 += 2;

}

$3 = $4

Standard C++ (original version):

int ex1(int n)

{

int reg[32] = {0,};

reg[2] = n;		// IN

reg[4] = 0;

reg[5] = 1;

while(1)

{

if(reg[2] < reg[5]) reg[6] = 1;

else reg[6] = 0;

if(reg[6] != reg[0]) break;

reg[4] += reg[5];

reg[5] += 2;

}

reg[3] = reg[4];

return reg[3];	// OUT

}

Standard C++ (simplified version):

int ex1_2(int n)

{

int a = 0;

int b = 1;

while(b <= n)

{

a += b;

b += 2;

}

return a;

}

What it does (in one sentence, as requested): Computes (floor((n+1)/2))2.

Explanation:

Looking at ex1_2 (the simplified version), it's apparent that we're computing:

sum i=(1,floor((n+1)/2)) [2i - 1]

Consider:

If n is odd, we stop at the first i s.t.:

2i - 1 > n

2i > n+1

i > (n+1)/2

i = (n+1)/2 + 1

i = floor((n+1)/2) + 1

Example: n = 5

We stop when: i = 4

If n is even, we stop at the first i s.t.:

2i - 1 > n

2i > n + 1

i > (n+1)/2

i = floor((n+1)/2) + 1

Example: n = 4

We stop when: i = 3

In both cases, we're stopping when i = floor((n+1)/2) + 1

Returning to our original sum, we have:

2*sum i=(1,floor((n+1)/2)) [i] - floor((n+1)/2)

= 2*((floor((n+1)/2))*((floor((n+1)/2))+1))/2 - floor((n+1)/2)

= floor((n+1)/2)2

As required.

2.

(i)

void ex2(int a, int b)

{

int q,r;

assert(a >= 0);

assert(b > 0);

q = 0;

r = a;

while(r >= b)

{

r -= b;

++q;

}

assert(a == q*b+r);

assert((0 <= r) && (r < b));

printf("%i %i\n", q, r);

}

(ii)

# Assume input as follows: $2 = a, $3 = b

begin:

li $4, 0				# $4 = 0						{q = 0}

add $5, $2, $0			# $5 = $2 + $0 = a + 0 = a			{r = a}

loop:

slt $6, $5, $3			# $6 = if $5 < $3 then 1 else 0		{$6 = if r < b then 1 else 0}

bne $6, $0, finish		# if $6 != $0 then goto finish		{$6 != $0 -> $6 != 0 -> r < b, so if

#							r < b, i.e. if !(r >= b), goto finish

#							(i.e. break)}

sub $5, $5, $3			# $5 = $5 - $3					{r = r - b -> r -= b}

addi $4, $4, 1			# $4 = $4 + 1					{q = q + 1 -> ++q}

br loop

finish:

# Outputs as follows: $4 = q, $5 = r

3.

(i)

unsigned long ex3(unsigned long *a, int n)

{

int i;

unsigned long max;

// Precondition: n > 0 && a[0..n) holds the array

assert(n > 0);

assert(a != NULL);	// safety first

i = 1;

max = a[0];

// Invariant: max is the maximum value in a[0..i)

while(i != n)

{

if(max < a[i])

{

max = a[i];

}

++i;

}

return max;

}

(ii)

# Assume input as follows: $2 = n

begin:

sll $2, $2, 2		# $2 = $2 * 4				{$2 = n * 4, because we're going to want to

#						compare it with i * 4}

li $3, 4			# $3 = 4					{$3 = i * 4 = 4 -> i = 1}

lw $4, a($0)		# $4 = a($0)				{max = a[0]}

loop:

beq $3, $2, finish	# goto finish if $3 = $2		{if(i * 4 == n * 4), i.e. if(i == n), goto finish

#						(i.e. break)}

lw $5, a($3)		# $5 = a($3)				{$5 = a[i]}

slt $6, $4, $5		# $6 = if $4 < $5 then 1 else 0	{$6 = if max < a[i] then 1 else 0}

addi $3, $3, 4		# $3 = $3 + 4				{++i}

beq $6, $0, loop		# goto loop if $6 = $0 = 0		{if(!(max < a[i])) then goto loop}

add $4, $5, $0		# $4 = $5 + $0 = $5 + 0 = $5		{max = a[i]}

br loop

finish:

# Output as follows: $4 = max

4.

See later.

5.

move $5, $3 ( add $5, $3, $0					# $5 := $3 + $0 = $3 + 0 = $3

clear $5 ( lui $5, 0x0000

li $5, small ( lui $5, 0x0000; addi $5, $5, small		# $5 := 0; $5 := $5 + small = 0 + small = small

li $5, big ( 		// TODO

lw $5, big($3)		// TODO

addi $...